### PART 1 – GENERAL

  - SUMMARY

- This section includes the following:

- Bicycle Parking Racks (U238 on Rails)

  - QUALITY ASSURANCE

A.	Installer Qualifications: An experienced installer who has completed installation of bicycle parking racks similar in material, design, and extent to that indicated for this project and whose work has resulted in construction with a record of successful in-service performance.

B.	Manufacturer Qualifications: A firm experienced in manufacturing bicycle parking racks similar to those required for this project and with a record of successful in-service performance.

- Source Limitations: Obtain each color, finish, shape and type of bicycle parking rack from a single source with resources to provide components of consistent quality in appearance and physical properties.

- Product Options: Drawings indicate size, shape and dimensional requirements of bicycle parking racks and are based on the specific system indicated.

  - REFERENCES

- Steel Pipe:

1.         ASTM A53 Standard Specification for Pipe, Steel, Black and Hot-Dipped, Zinc-Coated, Welded and Seamless

2.         ASTM A312 Standard Specification for Seamless and Welded Stainless Steel Pipes

- ASME SA312 Standard Specification for Seamless and Welded Stainless Steel Pipes

- B.	Steel Channel:

- ASTM A36 Standard Specification for Carbon Structural Steel

C.        Hot-Dipped Galvanized Finish:

1.        ASTM A123 Standard Specification for Zinc (Hot-Dipped Galvanized) Coating on Iron and Steel Products

  - SUBMITTALS

- Product Data: Include physical characteristics such as shape, dimensions, bicycle parking capacity and finish for each bicycle parking rack.

- Shop Drawings: Show installation details for each bicycle parking rack.

C.	Samples for Verification: For the following bicycle parking rack/s, showing; (1) the color of the powder coat finish. Prepare 2 inch by 3.5-inch (50.8 mm by 87.5mm) powder coat samples (or larger) from the same material to be used to finish the product, (2) the actual galvanized finish. Prepare a sample piece of sufficient size to judge its quality, (3) Stainless steel. Submit a sample piece for review.

D.        Maintenance Data: For each bicycle parking rack.

- Include recommended methods for repairing damage to the powder coat finish.

  - DELIVERY, STORAGE, AND HANDLING

- Store bicycle parking racks in original undamaged packages and containers until ready for installation.

B.        Handle powder coated bicycle parking racks with sufficient care to prevent any    scratches or damage to the finish.

  - WARRANTY

A. 	Bicycle parking racks are to carry a one year manufacturer’s limited warranty     against defects in materials and workmanship. The warranty period begins the date the product is shipped from the manufacturer.

### PART 2 - PRODUCTS

  - ACCEPTABLE MANUFACTURERS

A.	Provide bicycle parking racks manufactured by Madrax, a division of Graber Manufacturing, Inc.

  - MATERIALS

- Powder Coating: Triglycidyl isocyanurate (TGIC) powder, a polyester coating.

- Color as selected by architect from manufacturer’s full range of standard colors.

  - BICYCLE PARKING RACKS

- U238 on Rails:  The bicycle parking rack shall be the U238-__-__ (insert bicycle capacity and finish selection) bicycle parking rack as manufactured by Madrax, a division of Graber Manufacturing, Inc.

  - Hot-dipped galvanized (ASTM A123) or powder coated options: Rack shall be constructed of ASTM A53, 2” Schedule 40 steel pipe (2-3/8” O.D. x 0.154” thick wall (60.3mm x 3.9mm)) or better.

  - Stainless steel option: Rack shall be constructed of ASTM A312/ASME SA312, 2” Schedule 40S, TP 304 stainless steel pipe (2-3/8” O.D. x 0.154” thick wall (60.3mm x 3.9mm)).

  - Rails for all finish selections shall be ASTM A36, ‘C’ 3 x 4.1 channels (76.2mm x 35.8mm x 4.3mm) hot-dipped galvanized (ASTM A123).

PART 3 – EXECUTION

3.1       INSTALLATION

- Handle and install bicycle parking racks in accordance with manufacturer’s recommendations and installation instructions.

- Set bicycle parking racks secured to construction, level and true to line, in correct relationship to adjacent materials.